## Slide 1: Verifying MIPS Assembly Programs via Computational Tree Logic Model Checking
Darko Poposki, Risto Petroski, Dimitar Stojkovski, Guido Sciavicco

## Slide 2: Introduction
Formal verification of low level software;
Low level software is complex;
Software model checking;
Temporal logic:
  Linear
  Branching (Computational Tree Logic (CTL))
Application of this methodology to the verification of MIPS Assembly programs.

## Slide 3: Importance of Model Checking (1)
Therac-25 radiation machine for treatment of cancer patients (1985-87).

## Slide 4: Importance of Model Checking (2)
AT&T Telephone network problem in New York (1990).

## Slide 5: Importance of Model Checking (3)
Ariane 5 Crash (1996).

## Slide 6: What is Model Checking?
Model Checking is an automatic technique for verifying finite-state systems.

## Slide 7: MIPS Architecture and Assembly (1)
MIPS has 32 integer registers;
Data must be in registers to perform arithmetic;
31 of these are general-purpose registers that can be used in any of the instructions.

## Slide 8: MIPS Architecture and Assembly (2)
Limit to the following types of operations:
  Arithmetical operations
  Label definitions
  Unconditioned branches
  Conditioned branches
  Immediate operations
  Syscalls
Exclude the following:
  Defining functions
  Using the stack

## Slide 9: Example of Assembly Program
.text # Beginning of the instructions
main: # Starting label
li $t0, 1 # Load value 1 in register $t0
li $t1, 0 # Load value 0 in register $t1
beg_cycle: # Label for starting a cycle
bgt $t0, 10, end_cycle # $t0 > 10, go to label
add $t1, $t1, $t0 # $t1 = $t1 + $t0
add $t0, $t0, 1 # $t0 = $t0 + 1
b beg_cycle # Branch to beg_cycle
end_cycle: # Ending label

## Slide 10: Temporal Model of the Program

## Slide 11: Temporal Logic CTL (1)
Branch quantifiers:
  A (for all futures)
  E (for some future)
Future operators:
  G (always)
  F (sometime)
  X (nexttime)
  U (until)

## Slide 12: Temporal Logic CTL (2)
Checking over a MIPS program;
Consider the following property: it is never the case that a register is used if it has not been initialized before;
The formula corresponding to the above requirement is:
ᄀ(EU(ᄀi, a))

## Slide 13: The Verifier
Our system is designed into three connected parts:
  MIPS Program reading and model building;
  Safety requirement reading and tree-creation;
  Checking.

## Slide 14: Phases (1)
Phase 1.
  MIPS programs written in text files;
  Two boolean arrays: ValueSet and Accessed;
  Function sets the logical sequence of operations.
Phase 2.
  Formulas are supposed to be written in prenex - left first order;
  0ᄀEUᄀia
  A pointer is returned to the binary tree that represents the formula in question.

## Slide 15: Phases (2)
Phase 3.
  Checking for each level, for each (sub)formula at that level, and for each node of the structure;
  Answer positive – creating link to the corresponding node;
  At the end: if a pointer from the root of the structure to the root of the formula tree is present – formula is true in the current model.

## Slide 16: Example of Verification
ᄀ(EU(ᄀi, a))

## Slide 17: Program Model creation

## Slide 18: Formula Tree creation

## Slide 20: Conclusion
Formal verification of low level software is important;
Model checking CTL formulas to a specific problem;
This is the problem of formally checking MIPS Assembly simple programs;
Different programs;
Different kinds of temporal formulas;
This experiment partially covers the gap in formal verification of software for low level languages.

## Slide 21: References (1)
[1] S. Chaki. Sat-based software certification. In Proceedings of the 12th Conference on Tools and Algorithms for the Construction and Analysis of Systems (TACAS2006), pages 151-166, 2006.
[2] S. Chaki and J. Ivers. Software model checking without source code. ISSE, 6(3):233-242, 2010.
[3] E. Clarke, A. Groce, S. Jha, and H. Veith. Modular verification of software components in C. In Proceedings of ICSE 2003, pages 385-395, 2003.
[4] E. Clarke, D. Kroening, and F. Lerda. A tool for checking ANSI-C programs. In Proceedings of the 10th Conference on Tools and Algorithms for the Construction and Analysis of Systems (TACAS2004), pages 168-176, 2004.

## Slide 22: References (2)
[5] E. Allen Emerson. Temporal and modal logic. In HANDBOOK OF THEORETICAL COMPUTER SCIENCE, pages 995-1072. Elsevier, 1995.
[6] G. Holzmann. The SPIN Model Checker: Primer and Reference Manual. Addison-Wesley, 2003.
[7] Z. Manna and A. Pnueli. The Temporal Logic of Reactive and Concurrent Systems: Specification. Springer, 1992.
[8] N. Marti. Formal Verification of Low-Level Software. PhD thesis, 2008.
[9] A. Pnueli. Applications of temporal logic to the specification and verification of reactive systems: A survey of current trends. In Current Trends in Concurrency, pages 510-584. 1986.